2013 CALGREEN RESIDENTIAL CHECKLIST

MANDATORY ITEMS

COMMUNITY DEVELOPMENT DEPARTMENT – BUILDING  DIVISION

KIRK BALLARD, BUILDING OFFICIAL

ONE NORTH SAN ANTONIO ROAD ● LOS ALTOS, CA 94022-3088                            		   	  (650) 947-2752 ● FAX (650) 947-2734 ●  www.losaltosca.gov

PURPOSE:

The 2013 CALGreen Code applies to all newly constructed hotels, motels, lodging houses, dwellings, dormitories, condominiums, shelters, congregate residences, employee housing, factory-built housing and other types of dwellings with sleeping accommodations and new accessory buildings associated with such uses.  This section also applies to additions and alterations where there is an increase in conditioned space and specifies that these requirements only apply to the specific area of the addition or alteration. Existing site and landscaping improvements that are not otherwise disturbed are not subject to the requirements of CALgreen.

Project Name: ___________________________________________________________________________

Project Address: _________________________________________________________________________

Project Description: __________________________________________________________

Instructions:

1.  	 The owner or owner’s agent shall employ a licensed qualified green building professional experienced with the 2013                 	 California Green Building Standards Codes to verify and assure that all required work described herein is properly planned 	  and implemented in the project.

2.	 The licensed professional, in collaboration with the owner and the design professional shall review Column 2 of this

checklist, sign and date Section 1 –Design Verification at the end of this checklist., and have the checklist printed on the

approved plans for the project.

3.	 Prior to final inspection by the Building Department, the licensed professional shall complete Column 3

and sign and Date Section 2 – Implementation Verification at the end of this checklist and submit the completed form to

the Building Department.

| MANDATORY FEATURE OR MEASURE | COLUMN 2 Project Requirements | COLUMN 3 Verification |
| --- | --- | --- |
| Planning and Design Site Development |
| 4.106.2 A plan is developed and implemented to manage storm water drainage during construction. | x | □ |
| 4.106.3 Construction plans shall indicate how site grading or a drainage system will manage all surface water flows to keep water from entering buildings. | x | □ |
| General |
| 4.201.1 Building meets or exceeds the requirements of the California Building Energy Efficiency Standards3. | x | □ |

| Water Efficiency and Conservation Indoor Water Use |
| --- |
| 4.303.1. Plumbing fixtures (water closets and urinals) and fittings (faucets and showerheads) installed in residential buildings shall comply with the prescriptive requirements of Sections 4.303.1.1 through 4.303.1.4.4. | x | □ |
| 4.303.2 Plumbing fixtures and fittings required in Section 4.303.1 shall be installed in accordance with the California Plumbing Code, and shall meet the applicable referenced standards. | x | □ |
| Outdoor Water Use |
| 4.304.1 Automatic irrigation systems controllers installed at the time of final inspection shall be weather or soil moisture-based. | x | □ |

| Material Conservation and Resource Efficiency Enhanced Durability and Reduced Maintenance |
| --- |
| 4.406.1 Annular spaces around pipes, electric cables, conduits or other openings in plates at exterior walls shall be protected against the passage of rodents by closing such openings with cement mortar, concrete masonry or similar method acceptable to the enforcing agency. | x | □ |
| Construction Waste Reduction, Disposal and Recycling |
| 4.408.1 Recycle and/or salvage for reuse a minimum of 50 percent of the nonhazardous construction and demolition waste in accordance with one of the following: 1. Comply with a more stringent local construction and demolition waste management ordinance; or 2. A construction waste management plan per Section 4.408.2; or 3. A waste management company per Section 4.408.3; or 4. The waste stream reduction alternative per Section 4.408.4. | x | □ |
| Building Maintenance and Operation |
| 4.410.1 An operation and maintenance manual shall be provided to the building occupant or owner. | x | □ |

| ENVIRONMENTAL QUALITY Fireplaces |
| --- |
| 4.503.1 Any installed gas fireplace shall be a direct-vent sealed-combustion type. Any installed woodstove or pellet stove shall comply with US EPA Phase II emission limits where applicable. Woodstoves, pellet stoves, fireplaces shall also comply with applicable local ordinances. | x | □ |

| Pollutant Control |
| --- |
| 4.504.1 Duct openings and other related air distribution component openings shall be covered during construction. | x | □ |
| 4.504.2.1 Adhesives, sealants and caulks shall be compliant with VOC and other toxic compound limits. | x | □ |
| 4.504.2.2 Paints, stains and other coatings shall be compliant with VOC limits. | x | □ |
| 4.504.2.3 Aerosol paints and coatings shall be compliant with product weighted MIR limits for ROC and other toxic compounds. | x | □ |
| 4.504.2.4 Documentation shall be provided to verify that compliant VOC limit finish materials have been used. | x | □ |
| 4.504.3 Carpet and carpet systems shall be compliant with VOC limits. | x | □ |
| 4.504.4 80 percent of floor area receiving resilient flooring shall comply with the VOC-emission limits defined in the Collaborative for High Performance Schools (CHPS) High Performance Products Database or be certified under the Resilient Floor Covering Institute (RFCI) FloorScore program; or meet California Dept. of Public Health, “Standard Method for the Testing and Evaluation of Volatile Organic Chemical Emissions from Indoor Sources Using Environmental Chambers”, Version 1.1, February 2010 (also known as Specification 01350.) | x | □ |
| 4.504.5 Particleboard, medium density fiberboard (MDF) and hardwood plywood used in interior finish systems shall comply with low formaldehyde emission standards. | x | □ |
| Interior Moisture Control |
| 4.505.2 Vapor retarder and capillary break is installed at slab on- grade foundations. | x | □ |
| 4.505.3 Moisture content of building materials used in wall and floor framing is checked before enclosure. | x | □ |
| Environmental Comfort |
| Duct systems are sized, designed, and equipment is selected using the following methods: 1. Establish heat loss and heat gain values according to ANSI/ ACCA 2 Manual J-2004 or equivalent. 2. Size duct systems according to ANSI/ACCA 1Manual D-2009 or equivalent. 3. Select heating and cooling equipment according to ANSI/ACCA 3 Manual S-2004 or equivalent. | x | □ |

| Installer and Special Inspector Qualifications Qualifications |
| --- |
| 702.1 HVAC system installers are trained and certified in the proper installation of HVAC systems. | x | □ |
| 702.2 Special inspectors employed by the enforcing agency must be qualified and able to demonstrate competence in the discipline they are inspecting. | x | □ |
| Verifications |
| 703.1 Verification of compliance with this code may include construction documents, plans, specifications builder or installer certification, inspection reports, or other methods acceptable to the enforcing agency which show substantial conformance | x | □ |

1.  Green building measures listed in this table may be mandatory if adopted by a city, county, or city and county as

specified in Section 101.7

2.  Required prerequisite for this Tier.

3.  These measures are currently required elsewhere in statute or in regulation

CALGREEN SIGNATURE DECLARATIONS

Project Name:  ____________________________________________________________

Project Address:  __________________________________________________________

Project Description: _______________________________________________________________

SECTION 1 – DESIGN VERIFICATION Complete all lines of Section 1 – “Design Verification” and submit the entire checklist (Columns 2 and 3) with the plans and building permit application to the Building Department. The owner and design professional responsible for compliance with CalGreen Standards have reviewed the plans and certify that the items checked above are hereby incorporated into the project plans and will be implemented into the project in accordance with the requirements set forth in the 2013 California Green Building Standards Code as adopted by the City of Los Altos. ________________________________________________ _________________ Owner’s Signature Date ________________________________________________ Owner’s Name (Please Print) ______________________________________________________ ___________________ Design Professional’s Signature Date ______________________________________________________ Design Professional’s Name (Please Print) ______________________________________________________ ____________________ Signature of Licensed Professional responsible for CalGreen compliance Date ______________________________________________________ ____________________ Name of Licensed Professional responsible for CalGreen compliance (Please Print) Phone No. ______________________________________________________ Email Address for Licensed Professional responsible for CalGreen compliance

SECTION 2 – IMPLEMENTATION VERIFICATION Complete, sign and submit the completed checklist, including column 3, together with all original signatures on Section 2 to the Building Department prior to Building Department final inspection. I have inspected the work and have received sufficient documentation to verify and certify that the project identified above was constructed in accordance with this Green Building Checklist and in accordance with the requirements of the 2013 California Green Building Standards Code as adopted by the City of Los Altos. ____________________________________________________________ _____________________ Signature of Licensed Professional responsible for CalGreen Compliance Date ____________________________________________________________ _____________________ Name of Licensed Professional responsible for CalGreen compliance (Please Print) Phone No. __________________________________________________________________ Email address for Licensed Professional responsible for CalGreen compliance

** This form must be completed and returned to the City of Los Altos prior to your final inspection**